## Slide 1: Assembly Language Programming: 1. Introduction
.
Department of Computer Science & Engineering (CSE), United International University (UIU).

## Slide 2: Programming Languages
Machine Language
Assembly Language (Low Level Language)
High Level Languages
.
Department of Computer Science & Engineering (CSE), United International University (UIU).

## Slide 3: Simple Computer Model
.
Department of Computer Science & Engineering (CSE), United International University (UIU).

## Slide 4: Inside the CPU
.
Department of Computer Science & Engineering (CSE), United International University (UIU).

## Slide 5: CPU Registers
  General purpose registers
  Segment registers
  Instruction Pointer
  Flags register
  Special purpose registers
    Debug registers
    Machine Control registers
.
Department of Computer Science & Engineering (CSE), United International University (UIU).

## Slide 6
  AX (accumulator register):
  Stores operands for arithmetic & data transfer instructions.
BX Register (base register):
  Holds the starting base address of a memory within a data segment.
CX Register (counter register):
  Primarily used in loop instruction to store loop counter.
DX Register (data register)
  Used to contain I/O port address for I/O instruction.
General Purpose Registers

## Slide 7: General Purpose Registers (contd.)
Each of these 16-bit registers are further subdivided into two 8-bit registers.
AH | AL
BH | BL
CH | CL
DH | DL
AX
BX
CX
DX

## Slide 8
Memory Segmentation
Data Segment
  contains variable definitions
  declared by .DATA
Stack segment
  used to store the stack
  declared by .STACK size
  default stack size is 1KB.
Code segment
  contains program’s instructions
  declared by .CODE
  Extra segment
DS
CS
SS
ES
64 KB
64 KB
64 KB
8086 Memory
64 KB

## Slide 9: Flag Register
Flag register determines the current status of the microprocessor.
It is modified automatically by CPU after mathematical operations.
This allows to determine the type of the result.
8086 has 16-bit Flag register.
There are two kinds of flags: Status Flags and Control Flags

## Slide 10: Flag Register (contd.)
Status Flags | Control Flags
Carry Flag (CF) | Trap Flag
Auxiliary-carry Flag (AF) | Interrupt Flag
Zero Flag (ZF) | Directional Flag
Sign Flag (SF) | 
Parity Flag (PF) | 
Overflow Flag (OF) | 

## Slide 11: Flag Register (contd.)
Flag | Purpose
Carry (CF) | CF = 1 if there is a carry out from the MSB on addition or there is a Borrow into the MSB on subtraction.
Parity (PF) | PF=1 if the low byte of a result has an even number of one bits (even parity).
Auxiliary (AF) | Holds the carry (half–carry) after addition or borrow after subtraction between bit positions 3 and 4 of the result (for example, in BCD addition or subtraction.)
Zero (ZF) | Shows the result of the arithmetic or logic operation. Z=1; result is zero. Z=0; The result is 0
Sign (SF) | Holds the sign of the result after an arithmetic/logic instruction execution. SF=1 if the MSB of a result is 1.

## Slide 12: Flag Register (contd.)
Flag | Purpose
Trap (TF) | Enables the trapping through an on-chip debugging feature.
Interrupt (IF) | Controls the operation of the INTR (interrupt request) IF = 0 if the INTR pin is disabled IF = 1, if the INTR pin isenabled.
Direction (DF) | Selects either the increment or decrement mode for DI and /or SI registers during the string instructions.
Overflow (OF) | Overflow occurs when signed numbers are added or subtracted. An overflow indicates the result has exceeded the capacity of the machine.

## Slide 13
Stack Pointer (SP)
  A 16-bit register pointing to program stack
Base Pointer (BP)
  A 16-bit register used to access data in stack segment
  Usually used for based indexed or register indirect addressing
Source Index (SI) & Destination Index (DI)
  16-bit registers
  Used to point to memory locations in the data segment
Pointer and Index Registers

## Slide 14
Any Questions?
  Thank You
Department of Computer Science & Engineering (CSE), United International University (UIU).