## Slide 1: Arrays and Addressing Modes

## Slide 2: Array Addressing
1D Array
  W dw 10, 20, 30, 40
  X dw 100 dup(?)
  Y dw 5, 4, 3 dup(2, 3 dup(0), 1)
    5, 4 , 2, 0, 0, 0,1, 2, 0, 0, 0,1, 2, 0, 0, 0,1

## Slide 3: Array Addressing : 2D Array
Row Major:
  B dw 10, 20, 30, 40
      50, 60, 70, 80
      90, 100, 110, 120
Column Major:
  B dw 10, 50, 90, 130
      20, 60, 100, 140
      30, 70, 110, 150
      40, 80, 120, 160

## Slide 4: 2D Array (contd.)
If A is an MxN array; element size s byte
A[i,j] has address in
(i) row major order
  A + ((i-1)xN + (j-1)) x S

## Slide 5: Addressing Modes
The way an operand is specified

## Slide 6: Types of Addressing Modes
Register Mode
When an operand is a register
Example: Mov Ax, Bx ; src & dest both in register mode
Immediate Mode
When an operand is a constant
Example : Mov AX, 1
Direct Mode
When an operand is a variable
Example: Mov Ax, C

## Slide 7: Types of Addressing Modes(contd.)
Register Indirect
Offset address of an operand is contained in a register.
Offset : BX, SI, DI ; Segment # in DS
Offset: BP ; Segment # in SS
Example:
W dw 10, 20, 30
Mov ds, @data
Lea SI, W
Mov ax , [SI] ; ax 10
Add SI, 2 ; inc SI by 2 bytes/ 1 word as W is an word array
Mov ax, [SI] ; ax 20

## Slide 8: Types of Addressing Modes(contd.)
Assume,
  BX contains 1000h
  SI contains 2000h
  DI contains 3000h
  Offset 1OOOh contains 1BACh
  Offset 2000h contains 20FEh
  Ofiset 3000h contains 031Dh
Tell which of the following instructions are legal. If legal, give the source offset address and the result or number moved
  MOV BX, [BX]
  MOV CX, [SI]
  MOV BX, [AX]
  ADD [SI], [DI]
  INC [DI]

## Slide 9: Types of Addressing Modes(contd.)
Based /Indexed Addressing Mode
Array elements can be addressed in any of the following 4 ways:
Disp can be
[register + disp]
[disp + register]
[register] + disp
disp [register]
A variable
A constant
Variable + constant
Variable - constant
Ex . W
Ex . 2
Ex . W - 2
Ex . W + 2

## Slide 10: Based/ Indexed Addressing Mode(contd.)
Example :
  w dw 10, 20, 30, 40
  Mov bx, 2
  Mov ax, w[bx]
  ; interpreted as [w + bx], so ax = 20
  ; here disp[register] format has been used. All the 4 formats are interpreted as [ register + disp] or [disp + register]
  ; here w is disp and bx is register.
If BX or BP is used as register, then it is called Based Addressing Mode.
If DI or SI is used as register, then it is called Indexed Addressing Mode.

## Slide 11: Based Indexed Addressing Mode
Elements can be addressed as:
  Variable [BX or BP] [SI or DI]
  [BX or BP] + [SI or DI] + variable + constant
  Variable[BX or BP + SI or DI + constant]
  Constant [BX or BP + SI or DI + variable]
Whatever the format, the address is summation of all components.
W dw 10, 20, 30, 40, 50 ; bx has 2, SI has 4
Mov ax, w[BX + SI] ; ax = 40
Mov ax, w[BX + SI + 2] ; ax = 50

## Slide 12: Types of Addressing Modes(contd.)
Assume,
ALPHA DW 0123h, 0456h, 0789h, 0ABCDh
  BX contains 2
  SI contains 4
  DI contains 1
  Offset 0002h contains 1084 h
  Offset 0004h contains 2BAC h
  Tell which of the following instructions are legal. If legal, give the source offset address and the result or number moved
  MOV AX, [ALPHA+BX]
  MOV BX, ALPHA[SI]
  MOV BX, [BX+2]
  MOV AX, -2[SI]
  MOV AX, [BX]2
  ADD BX, [ALPHA+AX]